## Slide 2: Orchestrated Scheduling and Partitioning for Improved Address Translation in GPUs
Bingyao Li, Yueqi Wang, Xulong Tang
University of Pittsburgh
Notes: Hello everyone, I am Bingyao Li from university of Pittsburgh. It is great to here for sharing our work Orchestrated Scheduling and Partitioning for Improved Address Translation in GPUs

## Slide 3: Background
GPU are widely deployed in modern computing.
  Accelerate applications
  Explicitly manage data between CPU and GPU
Notes: GPUs are widely deployed in modern computing systems to provide acceleration for a wide range of applications, including machine learning, computer vision, social networks, and entertainment. However, traditional GPU execution requires significant programmer effort to explicitly manage the data and computation between CPUs and GPUs. Also, GPU has limited memory capacity, make it difficult to employ and manage for applications with large memory footprints.

## Slide 4: Background
GPU employs unified virtual memory (UVM) with demand paging.
  Ease programming
  Expensive address translation process
Notes: Recently, GPU vendors have proposed unified virtual memory, short name, UVM with demand paging to ease GPU programming. This feature is especially beneficial for executing applications which memory footprints exceed the GPU memory capacity. While UVM is promising, it introduces an expensive address translation process.

## Slide 5: Address Translation Process
SM
Interconnect
SM
SM
SM
MC
L2
MC
L2
MC
L2
Instruction $
Warp scheduler
SIMD lanes
Reg
file
Coalescing
L1 TLB
L1 D$
L2 TLB
L2 D$
Page table walk
1
2
4
3
5
6
Notes: This Figure shows GPU architecture and address translation process. Each GPU comprise multiple streaming multiprocessors (SMs) and memory partitions. Each SM has its own private L1 TLB and L1 cache. L2 TLB and L2 data cache are shared across all SMs and distributed across the memory partitions. So, the address translation process under unified virtual memory (UVM) is as follows. The memory requests generated by each thread are first coalesced by the GPU memory coalescing unit (1). The L1 data cache lookup happens in parallel with the L1 TLB lookup. If the translation is present in the L1 TLB, a TLB hit is returned and the physical page number is used to compare with the tags in the L1 cache (2). Otherwise, if the translation misses in the L1 TLB, the request is forwarded to the shared L2 TLB (3). If it further misses in the L2 TLB, the page table walker is triggered (4). After the physical address is obtained by walking the page table, the translation is populated to the shared L2 TLB (5) and further returned to L1 TLB (6) .

## Slide 6: Performance of L1 TLB
Chart: Hit rate
| bfs | color | mis | nw | pagerank | 3dconv | atax | bicg | gemm | mvt
64-entry | 0.53118 | 0.67368 | 0.52912 | 0.052953 | 0.61986 | 0.83499 | 0.29719 | 0.25882 | 0.90238 | 0.27682
256-entry | 0.7476 | 0.9175 | 0.8214 | 0.24347 | 0.96291 | 0.89911 | 0.73019 | 0.74009 | 0.99067 | 0.75484
Most of the GPU benchmarks suffer poor L1 TLB hit rates.
Adopting a larger L1 TLB improves the hit rates, while not scalable.
Notes: We study the GPU L1 TLB hit rates. This figure shows the L1 TLB performance, the hit rate under different L1 TLB entries. We can observe that, most of the GPU benchmarks suffer low L1 TLB hit rates. This is because a large number of memory pages are accessed intensively due to the GPU parallel execution. Since the private L1 TLB has limited capacity, the contention heavily thrashes the L1 TLB. So when we enlarge L1 TLB capacity from 64 to 256, it can be observed that many benchmarks benefit from larger L1 TLB capacity. While adopting a larger TLB improves the hit rates, it is not a scalable. Therefore, we focus on optimizations that do not increase the TLB capacity.

## Slide 7: Translation Reuses
Inter-TB
Intra-TB
Chart: 
| bfs | color | mis | nw | pagerank | 3dconv | atax | bicg | gemm | mvt
b1 | 0.87384 | 0.93217 | 0.9497 | 1 | 0.51268 | 0.96639 | 0 | 0 | 0 | 0
b2 | 0.050517 | 0.058566 | 0.036473 | 0 | 0.30188 | 0.0091213 | 1 | 1 | 0.97893 | 1
b3 | 0.072392 | 0.0059333 | 0.010585 | 0 | 0.18286 | 0.010334 | 0 | 0 | 0 | 0
b4 | 0.00069256 | 0.0012603 | 0.00045939 | 0 | 0.00082988 | 0.0061045 | 0 | 0 | 0.0012815 | 0
b5 | 0.0025593 | 0.0020728 | 0.002784 | 0 | 0.0017509 | 0.0080449 | 0 | 0 | 0.019786 | 0
Chart: 
| bfs | color | mis | nw | pagerank | 3dconv | atax | bicg | gemm | mvt
b1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
b2 | 4.2648e-05 | 0 | 0.00066243 | 0.51562 | 0 | 0 | 0 | 0 | 0 | 0
b3 | 0.00095957 | 0.016926 | 0.068909 | 0.48438 | 0.0027466 | 0.043177 | 0 | 0 | 0 | 0
b4 | 0.17594 | 0.35875 | 0.53243 | 0 | 0.093386 | 0.48627 | 0 | 0 | 0 | 0
b5 | 0.82306 | 0.62432 | 0.398 | 0 | 0.90387 | 0.47055 | 1 | 1 | 1 | 1
Most benchmarks show substantial intra-TB reuses rather than inter-TB reuses.
Notes: We next quantify the reuse potentials at inter-TB and intra-TB levels. We focus on TB as it is the granularity of computations that schedule on each SM. The y-axis in the figures represents the percentage of the total number of TBs. We divide the reuse intensity into 5 bins b1 to b5, with 20% increment for each bins. For example, b1 indicates that there are less than 20% of the total translations being reused, and b2 indicates there are more than 20% but less than 40% of the total translation being reused.
For inter-TB reuse, a TB pair is counted if the translation reuse are from two different TBs. For intra-TB reuse, a TB is counted the total number of translations reuse from the same TB.
We can see that while for some benchmarks, there are sizable inter-TB translation reuses, the majority of TBs in the benchmarks show significant intra-TB translation reuses rather than inter-TB reuses. So those reused translations are accessed multiple times during execution, bringing potentials for L1 TLB hits if the translation stays in the L1 TLB by the time it is being reused.

## Slide 8: Translation Reuses
Intra-TB
The 64-entry L1 TLB fails to capture most intra-TB translation reuses.
L1 TLB misses
Chart: CDF
| 2^3 | 2^4 | 2^5 | 2^6 | 2^7 | 2^8 | 2^9 | 2^10 | 2^11 | 2^12 | 2^13 | 2^14 | 2^15 | 2^16 | 2^17 | 2^18 | 2^19
bfs | 0.60727 | 0.64904 | 0.70453 | 0.76329 | 0.82416 | 0.89904 | 0.97399 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
color | 0.5436 | 0.63393 | 0.7276 | 0.83775 | 0.92199 | 0.975 | 0.99984 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
mis | 0.58635 | 0.64512 | 0.70984 | 0.78939 | 0.87165 | 0.96331 | 0.99989 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
nw | 0.46924 | 0.46924 | 0.49186 | 0.61732 | 0.95697 | 0.99811 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
pagerank | 0.54885 | 0.60413 | 0.70241 | 0.81502 | 0.92727 | 0.99768 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3dconv | 0.60606 | 0.65551 | 0.80214 | 0.9806 | 0.98707 | 0.99545 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
atax | 0.051401 | 0.055563 | 0.055563 | 0.14148 | 0.4582 | 0.98235 | 0.99961 | 0.99981 | 0.99984 | 0.99995 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1
bicg | 0.052892 | 0.055588 | 0.055588 | 0.11867 | 0.42904 | 0.95554 | 0.99961 | 0.9998 | 0.99984 | 0.99996 | 1 | 1 | 1 | 1 | 1 | 1 | 1
gemm | 0.0020411 | 0.094939 | 0.47089 | 0.96925 | 0.99886 | 0.99989 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
mvt | 0.051515 | 0.055562 | 0.055562 | 0.12577 | 0.47023 | 0.97354 | 0.99961 | 0.99981 | 0.99984 | 0.99995 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1
Notes: we next conduct translation reuse distance analysis to investigate whether the L1 TLB can capture these reuses during execution. Since a significant translation reuses are from intra-TB, We only show the distance analysis for intra-TB. We can see that the 64-entry L1 TLB fails to capture most intra-TB translation reuses.

## Slide 9: Translation Reuses
Intra-TB
Reducing the inter-TB interference can effectively reduce the reuse distances.
L1 TLB misses
Chart: CDF
| 2^3 | 2^4 | 2^5 | 2^6 | 2^7 | 2^8 | 2^9 | 2^10 | 2^11 | 2^12 | 2^13 | 2^14 | 2^15 | 2^16 | 2^17 | 2^18 | 2^19
bfs | 0.60727 | 0.64904 | 0.70453 | 0.76329 | 0.82416 | 0.89904 | 0.97399 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
color | 0.5436 | 0.63393 | 0.7276 | 0.83775 | 0.92199 | 0.975 | 0.99984 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
mis | 0.58635 | 0.64512 | 0.70984 | 0.78939 | 0.87165 | 0.96331 | 0.99989 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
nw | 0.46924 | 0.46924 | 0.49186 | 0.61732 | 0.95697 | 0.99811 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
pagerank | 0.54885 | 0.60413 | 0.70241 | 0.81502 | 0.92727 | 0.99768 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3dconv | 0.60606 | 0.65551 | 0.80214 | 0.9806 | 0.98707 | 0.99545 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
atax | 0.051401 | 0.055563 | 0.055563 | 0.14148 | 0.4582 | 0.98235 | 0.99961 | 0.99981 | 0.99984 | 0.99995 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1
bicg | 0.052892 | 0.055588 | 0.055588 | 0.11867 | 0.42904 | 0.95554 | 0.99961 | 0.9998 | 0.99984 | 0.99996 | 1 | 1 | 1 | 1 | 1 | 1 | 1
gemm | 0.0020411 | 0.094939 | 0.47089 | 0.96925 | 0.99886 | 0.99989 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
mvt | 0.051515 | 0.055562 | 0.055562 | 0.12577 | 0.47023 | 0.97354 | 0.99961 | 0.99981 | 0.99984 | 0.99995 | 0.99999 | 1 | 1 | 1 | 1 | 1 | 1
Chart: CDF
| 2^3 | 2^4 | 2^5 | 2^6 | 2^7 | 2^8 | 2^9 | 2^10 | 2^11 | 2^12 | 2^13 | 2^14 | 2^15 | 2^16 | 2^17 | 2^18 | 2^19
bfs | 0.67353 | 0.72207 | 0.77119 | 0.81716 | 0.86907 | 0.93638 | 0.98976 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
color | 0.72631 | 0.84703 | 0.91843 | 0.96211 | 0.98727 | 0.99811 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
mis | 0.74452 | 0.82776 | 0.89569 | 0.96012 | 0.98752 | 0.99878 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
nw | 0.46924 | 0.46924 | 0.98376 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
pagerank | 0.67079 | 0.78512 | 0.87057 | 0.95032 | 0.99022 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3dconv | 0.95668 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
atax | 0.055564 | 0.055564 | 0.055564 | 0.99957 | 0.99957 | 0.99979 | 0.9998 | 0.99983 | 0.99988 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
bicg | 0.055949 | 0.055949 | 0.055949 | 0.99957 | 0.99957 | 0.99979 | 0.9998 | 0.99983 | 0.99988 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
gemm | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
mvt | 0.055568 | 0.055568 | 0.055568 | 0.99957 | 0.99957 | 0.99979 | 0.99981 | 0.99984 | 0.99988 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Intra-TB removing inter-TB interference
Notes: As most TBs show more translation reuses within TBs rather than across TBs, concurrent execution of TBs on the same SM may cause severe interference and enlarge the translation reuse distances. To verify, we show the intra-TB reuse distance when inter-TB interference is removed. one can see that most of the benchmarks show reduced intra-TB reuse distances.
Our characterization reveals that, while there exist substantial intra-TB translation reuses, the reuse distances are generally large to yield good L1 TLB performance due to the inter-TB interference. Reducing the interference can effectively reduce the reuse distances, which can potentially translate to an improvement in the TLB hit rates.

## Slide 10: Proposed Optimization
Goal: improve L1 TLB hit rate by leveraging intra-TB translation reuses.
  TLB thrashing-aware TB scheduling
  Translation aware TLB Partitioning
  Dynamic and automatic TLB set sharing
Notes: The goal of this paper is to improve the GPU L1 TLB hit rate by leveraging intra-TB translation reuses. To this end, we propose i) TLB thrashing-aware TB scheduling that mitigates the inter-TB interference to effectively reduce the reuse distances, ii) TLB partitioning that isolates the translations oriented from different TBs to reduce TLB thrashing, and iii) dynamic and automatic TLB set sharing that accommodates the scenarios where adjacent TBs share translations.

## Slide 11: Proposal: TLB thrashing-aware TB scheduling
TB scheduling
L1 TLB thrashing?
low
Enough resource?
Yes
Schedule the TB on the SM
Choose next SM
high
No
Different SMs may have different L1 TLB hit rates because of the computation discrepancy among the TBs.
Notes: We first propose thrashing-aware TB scheduling. The baseline employs round-robin TB schedule. However, in some applications, especially in graph applications, the memory accesses among TBs are imbalanced. So, different SMs may have different L1 TLB hit rates because of the computation difference among the TBs.
So we enhance the baseline round-robin TB schedule with the capability to probe the instant L1 TLB miss rate. Whenever a new TB is to be scheduled, the scheduler first checks whether the candidate SM has a low TLB miss rate compared to other SMs. If so, it further checks the resource availability. Otherwise, the scheduler skips the SM and tries to find another SM with a low TLB miss rate. If the schedule cannot find an SM with low TLB miss rates, it falls back to the default scheduling.

## Slide 12: Proposal: TLB thrashing-aware TB scheduling
TB scheduling
L1 TLB thrashing?
low
Enough resource?
Yes
Schedule the TB on the SM
Choose next SM
high
No
Hardware Table to record
TLB accessing statistics
Different SMs may have different L1 TLB hit rates because of the computation discrepancy among the TBs.
Notes: We implement a hardware table for the TB scheduler to record the TLB hits and TLB total access for each SM to calculate the TLB miss rate. Each SM is responsible for updating the table based on its TLB accessing statistics.

## Slide 13: Proposal: Translation aware TLB partitioning
TBs scheduled on the same SM interfere with each other, enlarging intra-TB translation reuse distances.
Notes: Though the thrashing-aware TB scheduling tries to balance the number of translations across SMs and avoids oversubscription of particular SMs, it is still possible that the TBs scheduled on the same SM interfere with each other, therefore enlarging intra-TB translation reuse distances.

## Slide 14: Proposal: Translation aware TLB partitioning
L1 TLB partitioning based on the TBid instead of based on the address index bits.
Each TB within a SM will be associated with one set and the TBid is used to index the corresponding set.
Tag
PPN
v/d
Tag
PPN
v/d
Tag
PPN
v/d
Way 0
Way 1
Way 2
VPN
Page offset
1
2
TLB index
Compare
Mux
PPN
3
TB id
Notes: To address this problem, we propose L1 TLB partitioning based on the TB id instead of based on the address index bits. During GPU execution, each TB is labeled with a hardware TBid once it has been scheduled to an SM. The TBids are unique for the TBs running on the same SMs. When a TB finishes execution, the TBid is also freed for the next TB scheduled. In the TLB lookup process, the TBid is used to index the TLB sets (1). Then, the VPNs from all the TLB ways are compared with the VPN from the virtual address (2). If the comparison is successful, the corresponding PPN is retrieved from TLB to form a valid physical address. Similarly, in the TLB insertion process, the TBid is used to index the candidate set for the translation. If the sets are full, we use LRU algorithm for replacement.

## Slide 15: Proposal: Translation aware TLB partitioning
It can introduce redundant entries.
It can cause imbalanced numbers of translations in different TLB sets.
Tag
PPN
v/d
Tag
PPN
v/d
Tag
PPN
v/d
Way 0
Way 1
Way 2
VPN
Page offset
1
2
TLB index
Compare
Mux
PPN
3
TB id
Notes: While TLB partitioning mitigates the inter-TB interference, it may cause two problems that can affect the TLB hit rates. First, it can introduce redundant entries. For example, if TB 1 and TB 2 both access the same memory page, the same translation might be residing in different sets if TB 1 and TB 2 are not sharing the sets due to TBid based set indexing. Second, it can cause imbalanced numbers of translations in different TLB sets. some sets might get oversubscribed and experience higher miss rates, while others might be under-utilized due to fewer requests.

## Slide 16: Proposal: TLB set sharing
Tag
PPN
v/d
Tag
PPN
v/d
Tag
PPN
v/d
Way 0
Way 1
Way 2
VPN
Page offset
1
2
TLB index
Compare
Mux
PPN
3
TB id
Share reg
4
Notes: We then enhance our design with dynamic and automatic adjacent TLB set sharing. we design sharing flags held by a sharing register in the hardware. It is used to indicate whether the adjacent TBs should share their TLB sets or not.

## Slide 17: Proposal: TLB set sharing
Tag
PPN
v/d
Tag
PPN
v/d
Tag
PPN
v/d
Way 0
Way 1
Way 2
VPN
Page offset
1
2
TLB index
Compare
Mux
PPN
3
TB id
Share reg
4
TB1
TB2
TB3
TB4
Set1
Set2
Set3
Set4
Set5
Set6
Set7
Set8
Sharing register = 0000
Notes: Each TB has its own sharing flag indicating the sharing status with its neighboring TB.
Here is example. initially, the values of all sharing flags are set to 0, indicating that the TBid to the TLB set mapping is exclusive and there is no sharing between TBs

## Slide 18: Proposal: TLB set sharing
Tag
PPN
v/d
Tag
PPN
v/d
Tag
PPN
v/d
Way 0
Way 1
Way 2
VPN
Page offset
1
2
TLB index
Compare
Mux
PPN
3
TB id
Share reg
4
TB1
TB2
TB3
TB4
Set1
Set2
Set3
Set4
Set5
Set6
Set7
Set8
Sharing register = 1000
Notes: If TB1 shares the TLB sets indexed to TB2, the sharing flag of the first TB is set to 1. Sharing the sets among multiple TBs can reduce the thrashing of particular sets and balance the number of translations across multiple sets.

## Slide 19: Methodology
Simulator: gem5-gpu [CAL 15’]
Workloads: 10 benchmarks from Rodinia, poly-bench , and pannotia benchmark suites.
Baseline setup:
 | Configuration
GPU config | 16 SMs
Schedule | Greedy-Then-Oldest (GTO) dual warp schedule Round-Robin (RR) TB scheduler
TLB config | L1: 64 entries, 4-way, 1-cycle lookup latency L2: 512 entries, 16-way, 10-cycle lookup latency
Notes: We use gem5-gpu and 10 benchmarks from various GPU benchmark suites to evaluate our proposed optimizations. the detailed simulation configuration can be found in our paper.

## Slide 20: Evaluation
Chart: Normalized execution time
| bfs | color | mis | nw | pagerank | 3dconv | atax | bicg | gemm | mvt | GEOMEAN
scheduling | 0.99351 | 0.96384 | 0.99564 | 0.98484 | 0.99524 | 1.0028 | 0.98513 | 0.94159 | 0.983 | 0.93216 | 0.97751
scheduling+partitioning | 1.0455 | 1.5043 | 1.2352 | 0.96792 | 1.3428 | 1.1161 | 0.86885 | 0.78334 | 2.2025 | 0.90495 | 1.1435
scheduling+partition+sharing | 0.97833 | 0.89652 | 0.96355 | 0.96522 | 0.87659 | 0.90274 | 0.86885 | 0.78334 | 0.66381 | 0.90495 | 0.87528
Scheduling reduces the execution time by an average of 2.3%.
Notes: This figure shows the performance of each optimizations. First, scheduling reduces the execution time by an average of 2.3%. Though the improvement is marginal, the scheduling enlarges the potential for the subsequent TLB management.

## Slide 21: Evaluation
Chart: Normalized execution time
| bfs | color | mis | nw | pagerank | 3dconv | atax | bicg | gemm | mvt | GEOMEAN
scheduling | 0.99351 | 0.96384 | 0.99564 | 0.98484 | 0.99524 | 1.0028 | 0.98513 | 0.94159 | 0.983 | 0.93216 | 0.97751
scheduling+partitioning | 1.0455 | 1.5043 | 1.2352 | 0.96792 | 1.3428 | 1.1161 | 0.86885 | 0.78334 | 2.2025 | 0.90495 | 1.1435
scheduling+partition+sharing | 0.97833 | 0.89652 | 0.96355 | 0.96522 | 0.87659 | 0.90274 | 0.86885 | 0.78334 | 0.66381 | 0.90495 | 0.87528
Simple partitioning of the TLB degrades the performance of most benchmarks due to the reduced number of available entries to each TB.
Notes: Second, simple partition of the TLB degrades the performance of most benchmarks. This is because the number of available entries to each TB is reduced after partitioning.

## Slide 22: Evaluation
Chart: Normalized execution time
| bfs | color | mis | nw | pagerank | 3dconv | atax | bicg | gemm | mvt | GEOMEAN
scheduling | 0.99351 | 0.96384 | 0.99564 | 0.98484 | 0.99524 | 1.0028 | 0.98513 | 0.94159 | 0.983 | 0.93216 | 0.97751
scheduling+partitioning | 1.0455 | 1.5043 | 1.2352 | 0.96792 | 1.3428 | 1.1161 | 0.86885 | 0.78334 | 2.2025 | 0.90495 | 1.1435
scheduling+partition+sharing | 0.97833 | 0.89652 | 0.96355 | 0.96522 | 0.87659 | 0.90274 | 0.86885 | 0.78334 | 0.66381 | 0.90495 | 0.87528
Simple partitioning of the TLB degrades the performance of most benchmarks due to the reduced number of available entries to each TB.
Suffer from severe inter-TB interference, partitioning isolated the translations from different TBs.
Notes: However, for benchmarks atax, bicg, nw, and mvt, partitioning improves the overall application performance. This is because most of these benchmarks suffer from severe inter-TB interference, and partitioning isolated the translations from different TBs, hence reducing the interference.

## Slide 23: Evaluation
Chart: Normalized execution time
| bfs | color | mis | nw | pagerank | 3dconv | atax | bicg | gemm | mvt | GEOMEAN
scheduling | 0.99351 | 0.96384 | 0.99564 | 0.98484 | 0.99524 | 1.0028 | 0.98513 | 0.94159 | 0.983 | 0.93216 | 0.97751
scheduling+partitioning | 1.0455 | 1.5043 | 1.2352 | 0.96792 | 1.3428 | 1.1161 | 0.86885 | 0.78334 | 2.2025 | 0.90495 | 1.1435
scheduling+partition+sharing | 0.97833 | 0.89652 | 0.96355 | 0.96522 | 0.87659 | 0.90274 | 0.86885 | 0.78334 | 0.66381 | 0.90495 | 0.87528
TLB set sharing effectively improves the execution time.
The average execution time of all combined optimizations reduces by 12.5%.
Notes: Finally, when applying TLB set sharing, the average execution time reduces by 12.5%. This indicates that the proposed set sharing is able to improve the utilization of each TLB set while keeping the inter-TB interference reduced. More results can be found in our paper, such as adopting large pages and comparison with state of the art

## Slide 24: Summary
Problem: Address translation overheads in GPU systems under unified virtual memory.
Key idea: address translation TB level reuse
Proposal:
TB scheduling reduces the reuse distances
TLB partitioning reduces TLB thrashing
TLB set sharing accommodates adjacent TBs share translations
Improves performance by 12.5% on average.
Notes: In this paper, we mainly focus on address translation overhead in GPU systems under UVM. We leverage the TB level sharing to mitigate TLB thrashing. We propose three optimizations, including TB scheduling to reduce the reuse distances. TLB partitioning to mitigate the inter-TB interference. And TLB set sharing to accommodate those TBs that have translation sharing.
The results show that our proposed approach Improves performance by 12.5% on average.

## Slide 25
Thanks! Q&A
Orchestrated Scheduling and Partitioning for Improved Address Translation in GPUs
Bingyao Li, Yueqi Wang, Xulong Tang
Email: bil35@pitt.edu
Notes: That’s all about our paper. Thank you for listening my presentation,
I’ll happy to take any the questions.