## Slide 1: STAR: Sub-Entry Sharing-Aware TLB f​or Multi-Instance GPU
Bingyao Li1, Yueqi Wang1, Tianyu Wang1, Lieven Eeckhout2, Jun Yang1, Aamer Jaleel3, Xulong Tang1
1University of Pittsburgh, 2Ghent University, 3NVIDIA

## Slide 2
GPU Underutilization  MIG
GPUs are everywhere in the cloud ..
… but, they are severely underutilized
[1] https://dl.acm.org/doi/pdf/10.1145/3542929.3563510
e.g., Graph neural network for quantum chemistry -- 45% [1]
What is a potential solution?
GPU resource sharing allows better utilization
Notes: Major cloud providers like AWS, Google Cloud, offer GPUs on demand.
GPUs in the cloud are usually underutilized.
for example, below 45%
not all workloads can fully exploit this parallelism
so how to solve this problem?
one effective way is to enable GPU resource sharing among multiple applications.

## Slide 3
MIG to Improve Utilization
Multi-Instance GPU (MIG)
[2] https://docs.nvidia.com/datacenter/tesla/mig-user-guide/index.html
resource isolation, security …
SM
Notes: the Multi-Instance GPU is a promising solution.
It splits a single GPU into multiple independent instances, each GPU instance has its own system pipeline, SM, cache, and DRAM.
MIG stands out as it provides a very good isolation and security.

## Slide 4
Problem with MIG
GPU Instances share the on-chip Last-level TLB (L3 TLB)
Chart: Normalized performance
| CONV | MT | ST | VGG | ResNet | ResNext | DenseNet | DenseNet | VGG | ResNet | 3:2:2 | 3:3
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Single | 0.77907 | 0.75759 | 0.76681 | 0.76324 | 0.76852 | 0.81868 | 0.85975 | 0.88746 | 0.78299 | 0.90063
Performance of co-running applications on NVIDIA’s A100.
Shared TLB dynamically allocates resources based on the demand
Lead to TLB contention among multi-tenancy
TLB contention limits performance
Notes: MIG isn’t perfect partition every component. the Last-Level TLB (L3 TLB) didn’t divided.
The good thing
But, If multiple applications demand TLB entries, end up competing for shared TLB resources.
how this L3 TLB sharing impact on performance in the real case.
difference between running alone and co-running comes from how the L3 TLB is used. When an application runs alone, it gets exclusive access to the TLB. But when applications run together, they compete for TLB entries.

## Slide 5
TLB Structure
64 KB page
Lead to TLB contention among multi-tenancy
Virtual Base
Address
Valid/
Dirty
16 Sub-entries
L3 TLB entry
1 MB range
Contiguous in virtual address
Good for isolated workloads that use large contiguous memory
What are the implications under a multi-tenant setup?
[3] Zhang, Z., Allen, T., Yao, F., Gao, X., & Ge, R. TunneLs for Bootlegging: Fully Reverse-Engineering GPU TLBs for Challenging Isolation Guarantees of NVIDIA MIG. In Proceedings of the 2023 ACM SIGSAC Conference on Computer and Communications Security.
Notes: Different from what we think before
every TLB entry now holds 16 individual one-to-one address mappings.
The benefit of that is by compressing multiple translations, reducing hardware overhead. This sub-entry TLB design performs well for isolated workloads that use large contiguous memory.
what happens dealing with a multi-tenant setup,

## Slide 6
TLB Structure
Virtual Base
Address
Valid/
Dirty
0xA00
Sub-entries
0xA01
0xB00
Memory access
App 1
0xA000
…
0xA00F
0xA010
…
0xA01F
Time
App 1
Notes: All the sub-entries in these two TLB entries get completely filled

## Slide 7
TLB Structure
Virtual Base
Address
Valid/
Dirty
Memory access
0xA00
Sub-entries
0xA01
App 1
0xA000
…
0xA007
…
0xA00F
0xA010
…
0xA019
…
0xA01F
App 2
0xB000
…
0xB007
0xB00
TLB entries full
eviction
underutilized
Time
App 1
App 3
0xC000
…
Multi-tenancy interference causes TLB sub-entry underutilization
Notes: Now, we have multiple applications.

## Slide 8
TLB Sub-Entry Utilization
Chart: 
| HHH | HHM | HMM | HML | MMM | LLL
Single | 0.65248 | 0.65248 | 0.75139 | 0.76632 | 0.99159 | 0.99128
Co-run | 0.14479 | 0.11425 | 0.10697 | 0.17312 | 0.58131 | 0.94994
Category applications into High, Medium, Low based on their L2 TLB MPKI values
Substantially lower utilization under co-running compared to isolated run
Notes: we quantify the utilization of TLB sub-entries when applications are run alone versus when they are run together.
addressing this drop in utilization will be key to improving performance in MIG environments.

## Slide 9
Problem:
Problem Summary
  TLB sub-entry underutilized due to multi-tenancy interference
Goal:
  Improve TLB performance in MIG by enhancing sub-entry utilization
  MIG performance is hampered by TLB sharing
Notes: to brief summarize where are we.
we identified problem of xxx

## Slide 10
STAR (Sub-enTry shAring-awaRe TLB)
Allow two different bases sharing one TLB entry
Page offset
TLB index
virtual page base
sub-entry
index
Virtual address
L3 TLB entry
Base 1
Sub-entries
Base 2
v/d
v/d
How to support sharing ?
Notes: The key idea behind STAR is to allow two different base addresses to share the same TLB entry.
So, how do we support this sharing? I’ll first introduce the format of our TLB. 4 -> 3 bits

## Slide 11
STAR – TLB Format
Page offset
TLB index
virtual page base
sub-entry
index
Virtual address
L3 TLB entry
Base 1
Sub-entries
Base 2
v/d
v/d
0/1
2 pages share one sub-entry
Which one is occupying ?
Allow two different bases sharing one TLB entry
How to support sharing ?
Notes: only one can be stored in this slot. And we don’t know which translation is occupying the slot.

## Slide 12
STAR – TLB Format
Page offset
TLB index
virtual page base
sub-entry
index
Virtual address
L3 TLB entry
Base 1
Sub-entries
Base 2
v/d
v/d
0/1
Address Identify Bit (AIB)
compare
Allow two different bases sharing one TLB entry
How to support sharing ?
Notes: the AIB helps determine the access belongs to which translation.

## Slide 13
STAR – TLB Format & Sub-Entry Layout
Adaptive layout of sub-entry allocation
Applications show diverse access patterns, e.g., sequential, stride
sub-entry
index
Virtual
address
L3 TLB
entry
v/d
Base 1
v/d
Base 2
AIB
Sequential layout for contiguous access
sub-entry
index
AIB
v/d
v/d
Base 1
Base 2
Stride layout for interval access
Which layout to adopt?
01
10
layout-bit (‘00’ initial)
Notes: Considering applications have different memory access patterns, which two entry compete for same slot becomes important
based on the usage patterns observed.
To identify which layout is adopting, what bit used to index position, we also introduce a layout-bit.

## Slide 14
STAR – When to Share?
Less than half of the sub-entries are utilized
Only one base address is occupying the entry
v/d
Base 1
v/d
Base 2
01
v/d
Base
00
Notes: Now we know the basic TLB format of our approach. it’s important to know when sharing should happen.

## Slide 15
STAR – When to Share?
Dynamic shifts between the shared and non-shared state
v/d
Base 1
v/d
Base 2
01
v/d
Base 1
00
Application with increasing demand -> exclusively use
Notes: But application demand always change. also supports dynamic shifts between shared and non-shared states to adapt to changing workloads.

## Slide 16
STAR – Lookup Process
set m
 | Base 1 | 0 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Base 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ... |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
way-n
Virtual address
sub-entry
index
AIB
1
2
4
3

## Slide 17
STAR – Insertion process
 | Base 1 | 0 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Base 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ... |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Virtual address
sub-entry
index
AIB
replace
occupied
Scenario 1: Base hit, sub-entry empty
1
Scenario 2: Base hit, sub-entry occupied
Scenario 3: Base miss
2
 | Base 1
 | Base 2
1 0
3
stride access
Notes: the first case, If the base address is found in the TLB, and there is an available sub-entry.
If the base is found, but the sub-entry is already occupied
If the requested base is not present in the TLB

## Slide 18
Methodology
Simulator: MGPUSim [ISCA 2019]
Workloads:
  Applications classified by L2 TLB MPKI into High, Medium, and Low
  Each workload contains 3 applications
  Nine classes of workloads

## Slide 19
Evaluation – Overall Performance
STAR improves performance by an average of 28.7%
Chart: Normalized performance
| W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8 | W9 | W10 | W11 | HHH | HHM | HMM | HML | HLL | MMM | MML | MLL | LLL
 | 1.2747 | 1.5199 | 1.5106 | 1.3331 | 1.2649 | 1.2949 | 1.2443 | 1.117 | 1.1571 | 1.2195 | 1.0163

## Slide 20
Evaluation – Sub-entry Utilization
Chart: 
| W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8 | W9 | W10 | W11 | HHH | HHM | HMM | HML | HLL | MMM | MML | MLL | LLL
baseline | 0.15329 | 0.11425 | 0.10697 | 0.17312 | 0.16411 | 0.19849 | 0.58131 | 0.74161 | 0.53375 | 0.80595 | 0.94994
STAR | 0.54547 | 0.47726 | 0.47688 | 0.5811 | 0.63968 | 0.78659 | 0.90994 | 0.91804 | 0.81024 | 0.96729 | 0.96097
STAR improves sub-entry utilization by an average of 31.4%

## Slide 21
More Design Details and Results
Process of shared/non-shared shifts
Design overheads
Sensitivity Studies
  stride size
  number of sharing bases
  instance sizes
  ......
Comparison to state-of-the art
Notes: area overheads and power consumption, which is negligible

## Slide 22
Summary
Problem: TLB performance in multi-instance GPU
STAR:
Sub-entry sharing-aware TLB allows multiple bases sharing one entry
Adaptive layout of sub-entry allocation
Dynamic switch between shared and non-shared states
Improves performance by 28.7% on average , with negligible complexity
Sub-entry underutilization in shared L3 TLB

## Slide 23: STAR: Sub-Entry Sharing-Aware TLB f​or Multi-Instance GPU
Thanks! Q&A
Bingyao Li1, Yueqi Wang1, Tianyu Wang1, Lieven Eeckhout2, Jun Yang1, Aamer Jaleel3, Xulong Tang1
1University of Pittsburgh, 2Ghent University, 3NVIDIA

## Slide 24
Evaluation – Hit Rate
STAR improves hit rate by an average of 32.8%
Chart: Hit rate
| MT | BICG | ATAX | MT | ATAX | ST | MT | NW | ST | MT_s | ST_s | FIR | MT_s | BFS | PR | MT_s | FFT | FIR | NW | C2D | ST_s | ST_s | NW | FFT | BFS | BFS | PR | ST_s | FIR | FFT | FFT | FFT | FIR | W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8 | W9 | W10 | W11
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Baseline | 0.080489 | 0.81418 | 0.81418 | 0.017038 | 0.78347 | 0.40886 | 0.014775 | 0.25627 | 0.35855 | 0.13666 | 0.61149 | 0.0067031 | 0.24236 | 0.4576 | 0.39836 | 0.22474 | 0 | 0.0064613 | 0.4589 | 0.3902 | 0.70783 | 0.73128 | 0.48752 | 0 | 0.57965 | 0.58543 | 0.4866 | 0.74736 | 0.0015106 | 0 | 8.1314e-05 | 8.1314e-05 | 0.030511
STAR | 0.16452 | 0.83977 | 0.83965 | 0.092878 | 0.82389 | 0.62163 | 0.094499 | 0.46963 | 0.50662 | 0.1853 | 0.78351 | 0.054154 | 0.34554 | 0.61781 | 0.56537 | 0.31364 | 4.6407e-05 | 0.084503 | 0.5812 | 0.63722 | 0.85167 | 0.90707 | 0.61779 | 2.9999e-05 | 0.70898 | 0.71067 | 0.69218 | 0.90736 | 0.030511 | 3.0464e-06 | 8.9081e-05 | 8.9067e-05 | 0.051635